## Slide 1
THE ROAD HOME
SATQuery AI · JAI 2026
Syapru Besi, Nepal · August 2026
Which roads and homes may need inspection?
A source-based investigation, with uncertainty visible.

## Slide 2
The observations
Sentinel-1 SAR: 16 → 28 August 2026
Optical RGB: 22 → 27 August 2026
Historical OSM: 25 August 2026
Terrain: retained Copernicus 90 m DSM
Different dates and valid populations remain separate.
Grid equality does not establish physical co-registration.

## Slide 3
Separate change candidates
WATER: 9.56 ha · 956 candidates / 99,858 valid pixels
2 mapped buildings · 185.846 m roads / bridges
DEBRIS PROXY: 10.41 ha · 1,041 / 30,239 valid pixels
71 mapped buildings · 1,458.934 m roads
Possible exposure, not confirmed damage or closure.
Do not sum infrastructure totals across layers.

## Slide 4
The working demonstration
Before → After → Water → Debris → Infrastructure → Terrain → Evidence
Show RGB, then toggle cyan water, copper debris and violet mapped buildings.
Ask the source question, inspect the trace and open the TIFF/CSV evidence.
RGB is verified for 10 of 17 retained examples; 7 remain unavailable.
Overlay switches change display, not measurements.

## Slide 5
Engineering evidence
258 Python tests passed
6 optical interaction contract tests passed
36 Nepal source/API checks passed
17 retained real examples inspected
All 15 frozen Nepal artifacts hash-verified
Earlier narrative browser checks passed. Latest RGB / fixed-shell rendered QA is incomplete.
The Nepal question workflow is deterministic; no AI model is invoked.

## Slide 6
Contributions and boundaries
Prior work: SATQuery specialists, Flood Lab science and saved Nepal observations.
JAI work: verified bridge, terrain context, deterministic tools, external intake,
independent evaluation, Nepal narrative and switchable source overlays.
Codex assisted implementation, tests and documentation.
Debris is an unvalidated vegetation-to-bare + NDVI-loss + SAR-change proxy.
Access NOT_ASSESSED. No depth, damage, evacuation or forecast claim.
Repository: github.com/Yoriichi-GOD/SATquery-AI